## Slide 1: ACT: Architectural Carbon Modeling Tools
@ MICRO 2024
Tutorial
Udit Gupta, Leo Han

## Slide 2: ACT Tutorial: Today
Time | Topic
1:00 – 1:15pm | Introductory remarks
1:15 – 1:30pm | Sustainable Computing: Motivation and Challenges
1:30 – 2:15pm | Overview of ACT: An Architectural Carbon Modeling Tool
2:15 – 2:45pm | Hands-on ACT demo
2:45 – 3:00pm | Extending ACT
3:00 – 3:30pm | Break
3:30 – 4:30pm | Invited Talks: Tools for Carbon Accounting
4:30 – 5:00pm | Discussion
5:00 – 5:05pm | Closing Remarks
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 3
Estimating the embodied footprint of 2 devices using ACT
Takeaways
ACT provides first-order approximation of LCAs that use old technology nodes (45nm NAND, 32nm CPU)
ACT enables architects to study new technology nodes
IC component | ACT vs. Dell R740 server LCA | ACT vs. Fairphone 3 mobile device LCA
Compute (processors, SoC’s) | Within 2.2x | Within 1.18x
Memory | Within 1.62x | Within 2.1x
Storage | Within 1.05-2.2x | 

## Slide 4
How to set up ACT
>$ git clone https://github.com/S4AI-CornellTech/ACT.git
>$ cd ACT/
>$ source setup.sh
>$ python3 model.py
[Fab logic] Carbon/area from energy consumed 1209.5
[Fab logic] Carbon/area from gasses 240
[Fab logic] Carbon/area from materials 500
[Fab logic] Carbon/area aggregate 2228.0
https://github.com/S4AI-CornellTech/ACT.git
Notes: Note: Add units

## Slide 5
Estimating embodied footprint of Fairphone 3
Full end to end example can be found here: https://github.com/S4AI-CornellTech/ACT/blob/main/exps/fairphone3/fairphone3.py
https://www.fairphone.com/wp-content/uploads/2020/07/Fairphone_3_LCA.pdf
# Make sure you are in root directory
>$ cd ACT
>$ python3 tutorial/fairphone3_tutorial.py
--------------------------------
ACT RAM + Flash 0.0 kg CO2 vs. LCA 11 kg CO2
ACT CPU 0.0 kg CO2 vs. LCA 1.07 kg CO2
ACT ICs 0.0 kg CO2 vs. LCA 5.3 kg CO2

## Slide 6
Finding die areas for ICs in the Fairphone 3
https://www.fairphone.com/wp-content/uploads/2020/07/Fairphone_3_LCA.pdf
# Main Fairphone integrated circuits' areas in mm^2
# https://www.fairphone.com/wp-content/uploads/2020/07/Fairphone_3_LCA.pdf
# Look at page 22 (Table 3-5)
fairphone3_IC_areas = []

## Slide 7
Specifying CPU, DRAM, SSD and Yield
https://www.fairphone.com/wp-content/uploads/2020/07/Fairphone_3_LCA.pdf
fairphone_cpu_area = 46.4 #mm^2
fairphone_ram = 4 # GB
fairphone_storage = 64 # GB
ic_yield = 0.875

## Slide 8
Setting up ACT for IC Logic
IC_Logic = Fab_Logic(
gpa = "95",
  carbon_intensity = "src_coal",
  process_node = 28,
  fab_yield=ic_yield)
gpa = {“95”, “99”}
carbon_intensity = {“src_{energy_source}”, “loc_{country}”}
process_node = {28, 20, 14, 10, 8, 7, 5, 3}
fab_yield = yield where 0 <= yield <= 1

## Slide 9
Setting up ACT for CPU Logic
IC_Logic = Fab_Logic(
gpa = "95",
  carbon_intensity = "src_coal",
  process_node = 28,
  fab_yield=ic_yield)
CPU_Logic = Fab_Logic(
gpa = "95",
carbon_intensity = "src_coal",
process_node = 28,
fab_yield=ic_yield)

## Slide 10
Setting up ACT for DRAM and SSD
# DRAM Logic node
DRAM = Fab_DRAM(
config = "ddr3_50nm", fab_yield=ic_yield)
# SSD Logic node
SSD = Fab_SSD(
config = "nand_30nm", fab_yield=ic_yield)
For all DRAM and SSD configs, see config files in /dram/ and /ssd/ folders

## Slide 11
Computing the IC Carbon Footprint
IC_Logic.set_area(sum(fairphone3_IC_areas)/100.)
# area in cm^2
CPU_Logic.set_area(fairphone_cpu_area/100.)
# area in cm^2
DRAM.set_capacity(fairphone_ram)
SSD.set_capacity(fairphone_storage)
packaging_intensity = 150 # gram CO2

## Slide 12
Estimating embodied footprint of Fairphone 3
# Make sure you are in root directory
>$ cd ACT
>$ python3 tutorial/fairphone3_tutorial.py
--------------------------------
ACT RAM + Flash 5.310285714285714 kg CO2 vs. LCA 11 kg CO2
ACT CPU 0.8992937142857143 kg CO2 vs. LCA 1.07 kg CO2
ACT ICs 5.691643885714286 kg CO2 vs. LCA 5.3 kg CO2

## Slide 13
Estimating embodied footprint of Dell R740
Full end to end example can be found here: https://github.com/S4AI-CornellTech /ACT/blob/main/exps/dellr740/dellr740.py
https://corporate.delltechnologies.com/content/dam/digitalassets/active/en/unauth/data-sheets/products/servers/lca_poweredge_r740.pdf
# Make sure you are in root directory
>$ cd ACT
>$ python3 tutorial/dellr740_tutorial.py
--------------------------------
ACT SSD main 0 kg CO2 vs. LCA 3373 kg CO2
ACT SSD secondary 0 kg CO2 vs. LCA 64.1 kg CO2
ACT DRAM 0 kg CO2 vs. LCA 533 kg CO2
ACT CPU 0 kg CO2 vs. LCA 47 kg CO2

## Slide 15: ACT Tutorial: Today
Time | Topic
1:00 – 1:15pm | Introductory remarks
1:15 – 1:30pm | Sustainable Computing: Motivation and Challenges
1:30 – 2:15pm | Overview of ACT: An Architectural Carbon Modeling Tool
2:15 – 2:45pm | Hands-on ACT demo
2:45 – 3:00pm | Extending ACT
3:00 – 3:30pm | Break
3:30 – 4:30pm | Invited Talks: Tools for Carbon Accounting
4:30 – 5:00pm | Discussion
5:00 – 5:05pm | Closing Remarks
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 16
Estimating embodied footprint of Nvidia A100
Full end to end example can be found here: https://github.com/S4AI-CornellTech /ACT/blob/main/exps/dellr740/dellr740.py
https://corporate.delltechnologies.com/content/dam/digitalassets/active/en/unauth/data-sheets/products/servers/lca_poweredge_r740.pdf
# Make sure you are in root directory
>$ cd ACT
>$ python3 tutorial/dellr740_tutorial.py
--------------------------------
ACT SSD main 0 kg CO2 vs. LCA 3373 kg CO2
ACT SSD secondary 0 kg CO2 vs. LCA 64.1 kg CO2
ACT DRAM 0 kg CO2 vs. LCA 533 kg CO2
ACT CPU 0 kg CO2 vs. LCA 47 kg CO2