## Slide 1: ACT: Architectural Carbon Modeling Tools
@ MICRO 2024
Tutorial
Leo Han
Udit Gupta

## Slide 2: ACT Tutorial: Today
Time | Topic
1:00 – 1:15pm | Welcome to the ACT tutorial!
1:15 – 1:30pm | Motivation: Understanding the source of computing’s emissions
1:30 – 2:15pm | Overview of ACT: An Architectural Carbon Modeling Tool
2:15 –2:45pm | Hands-on ACT demo’s
2:45 – 3:00pm | Extending ACT
3:00 – 3:30pm | Coffee break
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 3
Tackling computing’s carbon footprint requires optimizing emissions across hardware life cycles (manufacturing and operational use)
Notes: How have these advances affected computing’s overall environmental sustainability and more specifically carbon footprint.

## Slide 4
Tackling computing’s carbon footprint requires optimizing emissions across hardware life cycles (manufacturing and operational use)
But (unlike performance, power, energy) there is a distinct lack of architectural tools and infrastructure to quantify carbon
Notes: How have these advances affected computing’s overall environmental sustainability and more specifically carbon footprint.

## Slide 5
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)

## Slide 6
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)
Overview of ACT

## Slide 7
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)
Overview of ACT
Comparing ACT to other methodologies

## Slide 8
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)
Overview of ACT
Comparing ACT to other methodologies
Sustainability aware-design case studies

## Slide 9
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)
Overview of ACT
Comparing ACT to other methodologies
Sustainability aware-design case studies

## Slide 10
Arch. Carbon Model
Carbon–aware HW design metrics
Architectural Carbon Modeling Tools (ACT)

## Slide 11
Arch. Carbon Model
Carbon–aware HW design metrics
SW design &
performance
HW design &
power
Fab
Environmental
Architectural Carbon Modeling Tools (ACT)

## Slide 12
Arch. Carbon Model
Carbon–aware HW design metrics
SW design &
performance
HW design &
power
Fab
Environmental
Operational CO2
Embodied CO2
CO2 -aware
HW optimization
Architectural Carbon Modeling Tools (ACT)

## Slide 13
Architectural Carbon Model
Model
Hardware/software input

## Slide 14
Architectural Carbon Model
Performance/power/energy and
lifetime of hardware
Model
Hardware/software input

## Slide 15
Architectural Carbon Model
Performance/power/energy and
lifetime of hardware
Energy efficiency and
environment (carbon intensity)
Model
Hardware/software input

## Slide 16
Architectural Carbon Model
Performance/power/energy and
lifetime of hardware
Energy efficiency and
environment (carbon intensity)
Overhead of hardware
manufacturing
Model
Hardware/software input

## Slide 17
Embodied carbon of application processors (SoC’s)
Notes: We add the energy, chemicals, and materials used by the fab.
And factor in yield of manufacturing

## Slide 18
Embodied carbon of application processors (SoC’s)
Hardware design
Energy
source (grid)
Device and fab characterization
(industry fabs, device data)

## Slide 19
Embodied carbon of application processors (SoC’s)
Fab energy increases over tech. nodes
DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)

## Slide 20
Embodied carbon of application processors (SoC’s)
95% abatement
99% abatement
TSMC (97%)
DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)
Fab energy increases over tech. nodes

## Slide 21
Embodied carbon of application processors (SoC’s)

## Slide 22
Embodied carbon of application processors (SoC’s)
Data sources:
[IMEC] DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)
[TSMC] TSMC Sustainability Reports 2018-2020

## Slide 23
Embodied carbon of application processors (SoC’s)
TSMC 2025 goal
(25% renewable)
Fab with coal
(0% renewable)
Fab with solar (100% renewable)
Data sources:
[IMEC] DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)
[TSMC] TSMC Sustainability Reports 2018-2020

## Slide 24
DRAM
from SK Hynix’s sustainability reports
Embodied carbon of DRAM memory

## Slide 25
Embodied carbon of DRAM memory
https://hotcarbon.org/assets/2024/pdf/hotcarbon24-final154.pdf

## Slide 26
NAND
from SK Hynix’s sustainability reports
Embodied carbon of NAND Flash storage

## Slide 27
HDD
from Seagate’s product environmental reports
Embodied carbon of HDD storage

## Slide 28
Additional details found in the paper…
ACT parameters
Notes: We take a similar approach for modeling emissions for memory and storage units which can be found in the paper.

## Slide 29
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)
Overview of ACT
Comparing ACT to other methodologies
Sustainability aware-design case studies

## Slide 30: Current carbon accounting methodologies
Economic Input/Output
(EIO)
Life cycle analysis
(LCA)
Carbon is tied directly to economic cost which is susceptible to market effects.
Current databases are out-of-date (45nm or older nodes).
LCA’s take high $$ and time to conduct.
Notes: EIO: A cost-based methodology to translate component price into embodied carbon footprint
LCA: A database-based methodology to quantify systems’ embodied emissions
Exergy: A methodology based on evaluating the thermodynamic energy in devices

## Slide 31
Comparing ACT with Apple’s product environmental reports
Apple iPhone
estimates
Apple iPad
estimates
ACT embodied
estimate
ACT embodied
estimate

## Slide 32
Comparing ACT with Apple’s product environmental reports
Apple iPhone
estimates
Apple iPad
estimates
ACT embodied
estimate
ACT embodied
estimate

## Slide 33
More comparisons (ACT vs. LCA’s) in the paper…
 | ACT vs. Dell R740 server LCA | ACT vs. Fairphone 3 mobile device LCA

## Slide 34
More comparisons (ACT vs. LCA’s) in the paper…
Takeaways
ACT provides first-order approximate of LCA’s that use old technology nodes (45nm NAND, 32nm CPU)
ACT enables architects to study new technology nodes
IC component | ACT vs. Dell R740 server LCA | ACT vs. Fairphone 3 mobile device LCA
Compute (processors, SoC’s) | Within 2.2x | Within 1.18x
Memory | Within 1.62x | Within 2.1x
Storage | Within 1.05-2.2x | 

## Slide 36
Challenge: How do we design sustainable systems by considering the footprint across lifecycles
This work: Architectural Carbon Modeling Tools (ACT)
Overview of ACT
Comparing ACT to other methodologies
Sustainability aware-design case studies

## Slide 37: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 38: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 39: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 40: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
Without renewables
during operation
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 41: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
DSP
optimal
Without renewables
during operation
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 42: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
Without renewables
during operation
With renewables
during operation
DSP
optimal
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 43: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
Without renewables
during operation
3x reduction
CPU
optimal
DSP
optimal
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 44: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 45: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Nvidia DL Accelerator (NVDLA)
Performance/energy vs.
Carbon

## Slide 46: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Nvidia DL Accelerator (NVDLA)
Performance/energy vs.
Carbon
30 FPS target
30 FPS target

## Slide 47: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Nvidia DL Accelerator (NVDLA)
Performance/energy vs.
Carbon
30 FPS target

## Slide 48: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Performance/energy vs.
Carbon
Nvidia DL Accelerator (NVDLA)
Energy
opt.
Performance
opt.
30 FPS target

## Slide 49: Reduce: Designing leaner hardware systems
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
Architectural
Carbon Model
Performance/energy vs.
Carbon
3x carbon decrease!
Nvidia DL Accelerator (NVDLA)

## Slide 50: Reduce: Designing leaner hardware systems
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
Architectural
Carbon Model
Performance/energy vs.
Carbon
2mm2 area
3x carbon decrease!
Nvidia DL Accelerator (NVDLA)

## Slide 51: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Performance/energy vs.
Carbon
2mm2 area
Nvidia DL Accelerator (NVDLA)
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
3x carbon decrease!

## Slide 52: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Performance/energy vs.
Carbon
2mm2 area
30% carbon increase
(Jevon’s paradox)
Nvidia DL Accelerator (NVDLA)
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
3x carbon decrease!

## Slide 53: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 54
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon

## Slide 55
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon
Embodied CO2
Operational CO2

## Slide 56
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon
Embodied
reduction
Operational
degradation
Embodied CO2
Operational CO2

## Slide 57
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon
Embodied
reduction
Operational
degradation
Embodied CO2
Operational CO2
Enabling 2nd life
requires enhancing
HW reliability
See paper for case
study on storage
reliability using
SSD overprovisioning

## Slide 58: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.
Application
OS/Run-time
Compiler
Architecture
Circuits
Devices &
Technology
Systems

## Slide 59: Leveraging Eco-Feedback for Carbon-Aware SLO’s
Application
OS/Run-time
Compiler
Architecture
Circuits
Devices &
Technology
Systems
Added latency delay (ms)
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 60: Attributing carbon footprint of cloud usage
Application
OS/Run-time
Compiler
Architecture
Circuits
Devices &
Technology
Systems

## Slide 61: Fairly attributing carbon
Application
OS/Run-time
Compiler
Architecture
Circuits
Devices &
Technology
Systems

## Slide 62: Fairly attributing carbon
Application
OS/Run-time
Compiler
Architecture
Circuits
Devices &
Technology
Systems
Operational Breakdown
Embodied Breakdown
Open research questions:
How do we fairly attribute operational and embodied carbon to individual cloud services?
How do we consider varying demand in data centers in attributing carbon responsibility?
How do we scale attribution mechanisms to cloud-scale?

## Slide 63: Uncertainty is inherent in carbon accounting

## Slide 64
Uncertainty is inherent in carbon accounting

## Slide 65: Uncertainty is inherent in carbon accounting
Open research questions:
What magnitude uncertainty exists across all IC components?
What degree of uncertainty exists in embodied versus operational carbon?
How do we consider uncertainty in carbon-aware hardware design to enable robust sustainable computing decisions?
*Attend our group’s talk “Understanding the Implications of Uncertainty in Embodied Carbon Models for Sustainable Computing” (Session 4)

## Slide 66: This work: ACT
Develop the model
Case studies

## Slide 67: This work: ACT
Develop the model
Case studies
More details in the paper!
Modeling parameters and industry sources for data
Carbon-aware metrics for early DSE (e.g., EDP, CDP, CEP)
Detailed comparison against industry LCA’s
Reuse case study: impact of reconfigurable accelerators (FPGA’s)
Recycle case study: Enabling second life & SSD provisioning

## Slide 68: Thank you!
Develop the model
Case studies
Open-source!
More details in the paper!
Modeling parameters and industry sources for data
Carbon-aware metrics for early DSE (e.g., EDP, CDP, CEP)
Detailed comparison against industry LCA’s
Reuse case study: impact of reconfigurable accelerators (FPGA’s)
Recycle case study: Enabling second life & SSD provisioning
This work: ACT

## Slide 69: ACT Tutorial: Today
Time | Topic
1:00 – 1:15pm | Welcome to the ACT tutorial!
1:15 – 1:30pm | Motivation: Understanding the source of computing’s emissions
1:30 – 2:15pm | Overview of ACT: An Architectural Carbon Modeling Tool
2:15 –2:45pm | Hands-on ACT demo’s
2:45 – 3:00pm | Extending ACT
3:00 – 3:30pm | Coffee break
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.