## Slide 1: ACT: Architectural Carbon Modeling Tools
@ MICRO 2022
Tutorial
Udit Gupta

## Slide 2: ACT Tutorial: Today
Time | Topic
1:00 – 1:15pm | Introductory remarks
1:15 – 1:30pm | Motivation: Understanding the source of computing’s emissions
1:30 – 2:15pm | Overview of ACT: An Architectural Carbon Modeling Tool
2:15 –2:30pm | Coffee Break
2:30 – 3:00pm | Hands-on ACT demo’s
3:00 – 3:15pm | Extending ACT
3:15 – 3:45pm | Office Hours
3:45 – 4:00pm | Closing remarks
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 3: ACT Tutorial: Today
Time | Topic
9:00 – 9:15am | Introductory remarks
9:15 – 9:30am | Motivation: Understanding the source of computing’s emissions
9:30 – 10:15am | Overview of ACT: An Architectural Carbon Modeling Tool
10:15 –10:30am | Coffee Break
10:30 – 11:00am | Hands-on ACT demo’s
11:00 – 11:15am | Extending ACT
11:15 – 11:45am | Office Hours
11:45 – 12:00pm | Closing remarks
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 4: Hyperscalar electricity consumption outpaces renewable growth
Source: Corporate sustainability reports and EIA

## Slide 5: Hyperscalar electricity consumption outpaces renewable growth
Source: Corporate sustainability reports and EIA

## Slide 6: Hyperscalar electricity consumption outpaces renewable growth
Hyperscalar CAGR 25% since 2015
USA Renewables CAGR 7% since 2015
Source: Corporate sustainability reports and EIA

## Slide 7: Today
Where does computing’s carbon footprint come from?
Notes: Specifically we ask the question, where does computing’s carbon footprint come from?
In our journey to answer this question what we found was quite surprising to some of our collaborators that have spent a lot of time thinking about hardware performance and energy efficiency optimizations.

## Slide 8: Today
Where does computing’s carbon footprint come from?
Mobile
Data center
Application
Notes: In particular we found that computing’s carbon footprint comes not only from energy consumed by running applications on hardware

## Slide 9: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Application
Notes: But also from manufacturing hardware devices.

## Slide 10: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 11: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 12: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Tackling computing’s emissions top down: enabling sustainable AI
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 13: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Tackling computing’s emissions top down: enabling sustainable AI
How can we curve computing’s emissions and enable sustainable computing (going beyond efficiency optimizations)?
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 14: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Tackling computing’s emissions top down: enabling sustainable AI
How can we curve computing’s emissions and enable sustainable computing (going beyond efficiency optimizations)?
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 15: Life Cycle Analysis: key to understanding carbon emissions
Notes: To study the breakdown of carbon emissions in mobile devices, we will use life cycle analyses or LCAs.
LCAs are frequently used to quantify the emissions across four phases of products.
This includes hardware systems.
The first phase is manufacturing the product, or hardware platform.

## Slide 16: Life Cycle Analysis: key to understanding carbon emissions
Notes: The second is transporting it from fabs to users.

## Slide 17: Life Cycle Analysis: key to understanding carbon emissions
Notes: The third is using the hardware mobile device.

## Slide 18: Life Cycle Analysis: key to understanding carbon emissions
Notes: The final phase is recycling and end of hardware life processing.
Portions of the hardware platforms can be repurposed for future iterations.

## Slide 19: Life Cycle Analysis: key to understanding carbon emissions
Energy consumption
Focus of systems, software, and hardware designers
“Opex”
Notes: When considering the carbon footprint of computing systems, systems, software, and hardware designers typically focus on product use or energy consumption.

## Slide 20: Life Cycle Analysis: key to understanding carbon emissions
Energy consumption
Focus of systems, software, and hardware designers
“Opex”
“Capex”
Hardware manufacturing
Emissions from fabs building chips
Overheads from infrastructure related activities
Overheads from operational energy consumption
Notes: However, through our analysis we find that for many use cases hardware manufacturing also contributes a significant portion of emissions to the overall hardware life cycle.
Where emissions from hardware use can be seen as opex-related emissions, we can think of emissions from manufacturing as capex-related footprint.

## Slide 21: Manufacturing dominates Apple’s overall carbon footprint
Notes: Here we look at the breakdown of Apple’s overall company-level footprint of 25 million metric tons of CO2 in 2019.
The hardware life cycle emissions are broken down into manufacturing shown in red, product use in green, transport in blue, and recycling in black.
In fact life cycle emissions account for nearly 98% of Apple’s footprint.

## Slide 22: Manufacturing dominates Apple’s overall carbon footprint
Manufacturing accounts for 74% of Apple’s end to end breakdown in 2019
Notes: As shown in red, Manfuacturing accounts for 74% of Apple’s end to end breakdown in 2019.

## Slide 23: Manufacturing dominates Apple’s overall carbon footprint
Manufacturing accounts for 74% of Apple’s end to end breakdown in 2019
Notes: Hardware use accounts for 19% of emissions.
Here, we find the majority of emissions are devoted to iOS devices like phones and tablets followed by macOS.
This includes emissions over the course of the entire life time of devices – typically 3 years for mobile phones.

## Slide 24: Manufacturing dominates Apple’s overall carbon footprint
Integrated circuits account for 33% of emissions (SoCs, DRAMs, NAND Flash)
Manufacturing accounts for 74% of Apple’s end to end breakdown in 2019
Notes: Within the manufacturing emissions, we find integrated circuits account for 33% of emissions.
This is more than the emissions due to boards/flexes, aluminum, displays, and other electronics.
These emissions are largely due to SoCs, DRAMs, NAND Flash components in mobile devices --- directly related to hardware design and development.

## Slide 25: Manufacturing dominates Apple’s overall carbon footprint
“Chasing Carbon: The Elusive Environmental Footprint of Computing” Gupta et. al. (HPCA 2021) https://arxiv.org/abs/2011.02839
Integrated circuits account for 33% of emissions (SoCs, DRAMs, NAND Flash)
Aggregating across hundreds of millions of phones, iPads, and other consumer devices sold every year!
Manufacturing accounts for 74% of Apple’s end to end breakdown in 2019
Notes: Now, these emissions are aggregated across hundreds of millions of phones, iPADs, and other consumer devices sold each year.
Next, we study the emission breakdowns for individual hardware platforms.

## Slide 26: Carbon footprint characteristics vary across devices
Data from public industry validated sustainability reports and life cycle analyses
Battery operated
Plugged in
Notes: So here we look at the carbon footprint breakdown of mobile devices.
On the x-axis we have 8 mobile devices. The first four are battery operated like iPads, iPhones, Apple Watches, and Laptops.
The last four are always connected or plugged in devices like personal assistants, desktops and gaming stations.
On the y-axis we have the absolute carbon footprint in log scale.
In black we see the end to end life cycle emissions, in red the manufacturing portion, and in green the emissions from hardware use and energy consumption.

## Slide 27: Carbon footprint characteristics vary across devices
Data from public industry validated sustainability reports and life cycle analyses
Battery operated
Plugged in
Roughly 75% life cycle emissions for battery operated devices comes from hardware manufacturing.
Notes: Across the battery operated devices we find that roughly 75% of emissions come from hardware manufacturing.

## Slide 28: Carbon footprint characteristics vary across devices
Emissions for always-connected devices come mainly from energy consumption
Roughly 75% life cycle emissions for battery operated devices comes from hardware manufacturing.
Data from public industry validated sustainability reports and life cycle analyses
Battery operated
Plugged in
Notes: On the other hand for plugged in devices we find the majority of emissions coming from energy consumption and roughly one third the footprint comes from hardware manufacturing.
We attribute the differences in carbon footprint breakdown across battery operated and always-connected devices to come from varying user behaviors such as frequency of use, different types of workloads, idle and sleep cycles, lifetime of hardware, and so on.
Another interesting point we see from this analysis is that the overall and manufacturing-related carbon footprints are not one-time, static costs.
Instead, they scale with hardware resources available in each platform.
In the paper you can find additional details about the carbon footprint breakdown across an even wider range of devices.
But for now, what I want to look at is another cross-section of this design space. Namely, how the carbon footprint of devices has been scaling over time.
### For example, the Mac Pro desktop without displays comprises the largest footprint given it comprises the largest hardware resources in terms of SoC capabilities, memory, and storage.

## Slide 29: Carbon footprint characteristics vary across devices
Emissions for always-connected devices come mainly from energy consumption
Roughly 75% life cycle emissions for battery operated devices comes from hardware manufacturing.
Data from public industry validated sustainability reports and life cycle analyses
Battery operated
Plugged in
1 “Latest Game Consoles: Environmental Winners or Losers?” National Resources Defense Council. Noah Horowitz
1 Xbox Standby mode consumes 4 billion kWh
Notes: On the other hand for plugged in devices we find the majority of emissions coming from energy consumption and roughly one third the footprint comes from hardware manufacturing.
We attribute the differences in carbon footprint breakdown across battery operated and always-connected devices to come from varying user behaviors such as frequency of use, different types of workloads, idle and sleep cycles, lifetime of hardware, and so on.
Another interesting point we see from this analysis is that the overall and manufacturing-related carbon footprints are not one-time, static costs.
Instead, they scale with hardware resources available in each platform.
In the paper you can find additional details about the carbon footprint breakdown across an even wider range of devices.
But for now, what I want to look at is another cross-section of this design space. Namely, how the carbon footprint of devices has been scaling over time.
### For example, the Mac Pro desktop without displays comprises the largest footprint given it comprises the largest hardware resources in terms of SoC capabilities, memory, and storage.

## Slide 30: Greenhouse gas (GHG) Protocol
Technology company
Notes: To study the breakdown of carbon emissions at the data center scale we use the green house gas protocol.
The GHG protocol is used by many companies including technology companies like Google, Facebook, Apple, Microsoft, and others.
The GHG protocol categories emissions into three main scopes.

## Slide 31: Greenhouse gas (GHG) Protocol
Technology company
Scope 1
Diesel, gas, refrigerant from facilities
Company-owned transport
Notes: First, Scope 1 quantifies emissions directly from burning diesel, gas, and refrigerants in facilities.

## Slide 32: Greenhouse gas (GHG) Protocol
Technology company
Scope 1
Diesel, gas, refrigerant from facilities
Company-owned transport
Scope 2
Purchased energy (renewables)
Notes: Scope 2 quantifies the emissions from purchased energy.
This includes the impact of buying renewable energy sources to offset the net or average carbon footprint from energy being consumed by data centers.
This net emission factor does not ensure that every unit of energy consumed by data centers comes from renewable energy but rather the average carbon intensity of energy consumed.

## Slide 33: Greenhouse gas (GHG) Protocol
Technology company
Scope 1
Diesel, gas, refrigerant from facilities
Company-owned transport
Scope 3 (Upstream)
Hardware and racks
Data center construction
Business travel
Scope 2
Purchased energy (renewables)
Notes: Finally, we have Scope 3 which comprises emissions from the supply chain.
Depending on the company, the supply chain can be separated into the upstream and down-stream supply chain.
The upstream primarily includes capital and purchased goods, business travel, and infrastructure setup.

## Slide 34: Greenhouse gas (GHG) Protocol
Technology company
Scope 1
Diesel, gas, refrigerant from facilities
Company-owned transport
Scope 3 (Upstream)
Hardware and racks
Data center construction
Business travel
Scope 2
Purchased energy (renewables)
Scope 3 (Downstream)
Use of sold goods
Transportation and distribution
Notes: On the other hand, the down stream supply chain and Scope 3 emissions comprise the use of sold goods and transportation and distribution of goods.
Note that in the context of data center oriented technology companies like Facebook and Google, Scope 3 emissions ar edominate dby the upstream footprint.

## Slide 35: Greenhouse gas (GHG) Protocol
Technology company
Scope 1
Diesel, gas, refrigerant from facilities
Company-owned transport
Scope 3 (Upstream)
Hardware and racks
Data center construction
Business travel
Scope 2
Purchased energy (renewables)
Scope 3 (Downstream)
Use of sold goods
Transportation and distribution
Scope 2 emissions come from opex-related activities
Scope 1 and Scope 3 emissions come from capex-related activities
Notes: Note that, in terms of data centers, Scope 2 emissions come from opex—related activities.
On the other hand, Scope 1 and Scope 3 emissions come from capex-related activites.

## Slide 36: Historical analysis of Facebook’s carbon footprint
Scope 1 - Capex
Scope 2 - Opex
Scope 3 - Capex
2014
2015
2016
2017
2018
2019
2020
2021
Location-based Emissions
Notes: Here we look at the historical trends in Facebook’s carbon footprint using the GHG protocol.
In blue we see net Scope 1 emissions.
In green, net Scope 2 emissions.
In red, net Scope 3 emissions.
On the x-axis we look at the breakdown between 2014 to 2019.

## Slide 37: Historical analysis of Facebook’s carbon footprint
Scope 1 - Capex
Scope 2 - Opex
Scope 3 - Capex
Impact of renewable energy in data centers
2014
2015
2016
2017
2018
2019
2020
2021
Notes: On the far right, we see the impact of Facebook purchasing renewable energy as the difference between the black dashed line and the green. We see Scope 2 emissions greatly reduce upon powering data centers with renewable energy.

## Slide 38: Historical analysis of Facebook’s carbon footprint
Scope 1 - Capex
Scope 2 - Opex
Scope 3 - Capex
Scope 3 (capex) dominates Facebook’s carbon emissions.
49% of Scope 3 comes from hardware, infrastructure, data center construction
Impact of renewable energy in data centers
2014
2015
2016
2017
2018
2019
2020
2021
Notes: Following the mobile analysis, we find that Scope 3 dominates Facebook’s carbon emissions.

## Slide 39: Historical analysis of Facebook’s carbon footprint
Scope 1 - Capex
Scope 2 - Opex
Scope 3 - Capex
Scope 3 (capex) dominates Facebook’s carbon emissions.
49% of Scope 3 comes from hardware, infrastructure, data center construction
Impact of renewable energy in data centers
Change in HW footprint disclosure practice
2014
2015
2016
2017
2018
2019
2020
2021
Notes: Interestingly we see a large increase in Facebook’s Scope 3 emissions between 2018 and 2019.
The increase is primarily due to a change in hardware footprint disclosure practices.
In particular prior to 2018, the carbon footprint related to emissions from manufacturing servers found in the data center were not included.
After 2018, hardware manufacturing emissions began to be included causing a stark rise in Scope 3 emissions.
The change disclosure practices highlight the need to motivate companies to report their carbon emissions over time.
In fact, we see similar trends across other data center oriented companies, like Google as outline din the paper below.

## Slide 40: Addressing Scope 3: Economic incentives and Carbon Sequestration
https://cloudblogs.microsoft.com/industry-blog/sustainability/2022/03/24/how-microsoft-is-using-an-internal-carbon-fee-to-reach-its-carbon-negative-goal/
Microsoft: $100/tCO2e to incentivize reductions
Google: Estimates $50-$300/tCO2e as carbon sequestration scales, up to 20% of the cost of a server!
https://www.youtube.com/watch?v=W7uTbxCxmPg

## Slide 41: Chip manufacturing is energy intensive
Source: 2021 corporate sustainability reports
Hyperscalar CAGR 25% since 2015
“Fab 4” CAGR 11% since 2015
USA Renewables CAGR 7% since 2015

## Slide 42
Semiconductor fab
Energy
(60%)
Chemicals (15%)
PFCs (10%)
Wafer & gas (10%)
Gupta et. al. Chasing Carbon: The Elusive Environmental Footprint of Computing (HPCA 2021)

## Slide 43
Semiconductor fab
100% Renewable powered semiconductor fab
Energy
(60%)
Chemicals (15%)
PFCs (10%)
Wafer & gas (10%)
Reduces manufacturing footprint by 2.5x
Gupta et. al. Chasing Carbon: The Elusive Environmental Footprint of Computing (HPCA 2021)

## Slide 44: “Green” powered fabs are not enough
Semiconductor fab
100% Renewable powered semiconductor fab
Energy
(60%)
Chemicals (15%)
PFCs (10%)
Wafer & gas (10%)
Reduces manufacturing footprint by 2.5x
TSMC plans for
25% renewable by 2025 and 100% renewable by 2050.
Gupta et. al. Chasing Carbon: The Elusive Environmental Footprint of Computing (HPCA 2021)

## Slide 45: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Tackling computing’s emissions top down: enabling sustainable AI
How can we curve computing’s emissions and enable sustainable computing (going beyond efficiency optimizations)?
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 46
Tackling computing’s carbon footprint requires optimizing emissions across hardware life cycles (manufacturing and operational use)
Notes: How have these advances affected computing’s overall environmental sustainability and more specifically carbon footprint.

## Slide 47
Tackling computing’s carbon footprint requires optimizing emissions across hardware life cycles (manufacturing and operational use)
But (unlike performance, power, energy) there is a distinct lack of architectural tools and infrastructure to quantify carbon
Notes: How have these advances affected computing’s overall environmental sustainability and more specifically carbon footprint.

## Slide 48
Arch. Carbon Model
Carbon–aware HW design metrics
Architectural Carbon Modeling Tools (ACT)

## Slide 49
Arch. Carbon Model
Carbon–aware HW design metrics
SW design &
performance
HW design &
power
Fab
Environmental
Architectural Carbon Modeling Tools (ACT)

## Slide 50
Arch. Carbon Model
Carbon–aware HW design metrics
SW design &
performance
HW design &
power
Fab
Environmental
Operational CO2
Embodied CO2
CO2 -aware
HW optimization
Architectural Carbon Modeling Tools (ACT)

## Slide 51
Architectural Carbon Model
Model
Hardware/software input

## Slide 52
Architectural Carbon Model
Performance/power/energy and
lifetime of hardware
Model
Hardware/software input

## Slide 53
Architectural Carbon Model
Performance/power/energy and
lifetime of hardware
Energy efficiency and
environment (carbon intensity)
Model
Hardware/software input

## Slide 54
Architectural Carbon Model
Performance/power/energy and
lifetime of hardware
Energy efficiency and
environment (carbon intensity)
Overhead of hardware
manufacturing
Model
Hardware/software input

## Slide 55
Embodied carbon of application processors (SoC’s)
Notes: We add the energy, chemicals, and materials used by the fab.
And factor in yield of manufacturing

## Slide 56
Embodied carbon of application processors (SoC’s)
Hardware design
Energy
source (grid)
Device and fab characterization
(industry fabs, device data)

## Slide 57
Embodied carbon of application processors (SoC’s)

## Slide 58
Embodied carbon of application processors (SoC’s)
Data sources:
[IMEC] DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)
[TSMC] TSMC Sustainability Reports 2018-2020

## Slide 59
Embodied carbon of application processors (SoC’s)
Fab with coal
(0% renewable)
Fab with solar (100% renewable)
Data sources:
[IMEC] DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)
[TSMC] TSMC Sustainability Reports 2018-2020

## Slide 60
Embodied carbon of application processors (SoC’s)
TSMC 2025 goal
(25% renewable)
Fab with coal
(0% renewable)
Fab with solar (100% renewable)
Data sources:
[IMEC] DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)
[TSMC] TSMC Sustainability Reports 2018-2020

## Slide 61
Additional details found in the paper…
Memory and storage
Data sources: SK Hynix, Apple
ACT parameters
DRAM
SSD
Notes: We take a similar approach for modeling emissions for memory and storage units which can be found in the paper.

## Slide 62
Comparing ACT with Apple’s product environmental reports
Apple iPhone
estimates
Apple iPad
estimates
ACT embodied
estimate
ACT embodied
estimate

## Slide 63
Comparing ACT with Apple’s product environmental reports
Apple iPhone
estimates
Apple iPad
estimates
ACT embodied
estimate
ACT embodied
estimate

## Slide 64: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 65: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 66: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 67: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
Without renewables
during operation
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 68: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
DSP
optimal
Without renewables
during operation
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 69: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
Without renewables
during operation
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases
DSP
optimal

## Slide 70: Reuse: General purpose versus custom mobile HW
Architectural
Carbon Model
Commodity (mobile CPU)
Specialized (mobile GPU, DSP)
Carbon per inference
Without renewables
during operation
3x reduction
CPU
optimal
DSP
optimal
With renewables
during operation
AI inference case study (MobileNet) assuming 3 year hardware lifetime, and same utilization in all cases

## Slide 71: Tenets of Environmental Design
Reduce
Reuse
Recycle
Design leaner footprint software and hardware.
Repurpose systems already produce.
Recover discarded systems and components.

## Slide 72: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Nvidia DL Accelerator (NVDLA)
Performance/energy vs.
Carbon

## Slide 73: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Nvidia DL Accelerator (NVDLA)
Performance/energy vs.
Carbon
30 FPS target
30 FPS target

## Slide 74: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Nvidia DL Accelerator (NVDLA)
Performance/energy vs.
Carbon
30 FPS target

## Slide 75: Reduce: Designing leaner hardware systems
Architectural
Carbon Model
Performance/energy vs.
Carbon
Nvidia DL Accelerator (NVDLA)
Energy
opt.
Performance
opt.
30 FPS target

## Slide 76: Reduce: Designing leaner hardware systems
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
Architectural
Carbon Model
Performance/energy vs.
Carbon
3x carbon decrease!
Nvidia DL Accelerator (NVDLA)

## Slide 77: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Tackling computing’s emissions top down: enabling sustainable AI
How can we curve computing’s emissions and enable sustainable computing (going beyond efficiency optimizations)?
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 78: Computing incurs a growing environmental footprint
1.2-2.2 Billion tons of CO2
Mobile
Communication
Data center
59% of world online
Future improvements challenging (e.g., slowing Moore’s law)
Emerging applications demanding higher compute
Notes: When we aggregate computing environmental impact across mobile, communication, and data centers, studies show that computing accounts for 900 million metric tons of CO2.
That’s on par with the aviation industry’s footprint and around 2-4% of worldwide emissions.
Not only is this a huge amount already but we find that ICT emissions are expected to double over the next decade given the growing demand for computing.
And so it’s crucial that we as a community start think about what it means for computing itself to be sustainable.

## Slide 79: AI growth imposes high infrastructure costs
Mobile systems have dedicated bionic accelerators accounting for ¼ of SoC area
Data center
AI accounts for ~15% of Google’s data center
Training and inference in Meta’s data center grown by 3x capacity in 2 years
Data capacity doubled in Meta’s data center
Mobile

## Slide 80: Growing literature quantifying AI emissions

## Slide 81: Growing literature quantifying AI emissions

## Slide 82
Training and experimentation
(29%)
Machine learning life cycle
Wu et. al. Sustainable AI: Environmental Implications, Challenges, and Opportunities (MLSys 2022)

## Slide 83: Crucial to look at emissions across ML cycle
Data
Collection (31%)
Training and experimentation
(29%)
Inference
(40%)
Machine learning life cycle
Wu et. al. Sustainable AI: Environmental Implications, Challenges, and Opportunities (MLSys 2022)

## Slide 84: Crucial to look at emissions across HW cycle

## Slide 85: Jevon’s paradox of AI at-scale
Baseline AI power capacity (Meta)
Optimized power capacity

## Slide 86: Today
Where does computing’s carbon footprint come from?
A combination of both energy consumed and hardware manufacturing (embodied carbon).
Mobile
Data center
Fabs
Application
Understanding the source of computing’s emissions
Tackling computing’s emissions bottom up: architectural carbon models
Tackling computing’s emissions top down: enabling sustainable AI
How can we curve computing’s emissions and enable sustainable computing (going beyond efficiency optimizations)?
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 87: Global-Scale Carbon Optimization

## Slide 88: Performance versus manufacturing footprint
Data from industry (Apple, Google, Huawei) life cycle analyses and GeekBench performance measurements https://www.geekbench.com/blog/2019/09/geekbench-5/
Notes: Here we study the tradeoff between performance and manufacturing related carbon emissions.
On the x-axis we have mobile Net v1 inference throughput gathered from Geekbench measurements.
On the y-axis we have manufacturing-related emissions gathered from publicly available sustainability reports from LCAs of devices with 128 GB capacity.
In yellow and green we have example mobile devices from 2015 and 2016.
H denotes devices from Huawei and A from apple.

## Slide 89: Performance versus manufacturing footprint
Data from industry (Apple, Google, Huawei) life cycle analyses and GeekBench performance measurements https://www.geekbench.com/blog/2019/09/geekbench-5/
Notes: Adding 2017 in blue, we find a pareto curve forming between mobile performance and manufacturing related carbon emissions.

## Slide 90: Performance versus manufacturing footprint
Between 2017 and 2019 the Pareto frontier has shifted to the right prioritizing performance.
Designing sustainable systems requires shifting the frontier down.
Data from industry (Apple, Google, Huawei) life cycle analyses and GeekBench performance measurements https://www.geekbench.com/blog/2019/09/geekbench-5/
Performance and efficiency improvement
Notes: Further analyzing devices from 2018 in black and 2019 in red, we find that the Pareto-frontier from 2017 and 2019 shifted strictly to the right.
As a result, while performance has improved, carbon footprint has not.
These performance advantages are a result of both algorithm and hardware improvements.
Moving forward we need to think about ways to not only shift this Pareto to the right, but also downwards to lower emissions.
This includes carbon-aware resource provisioning and increasing the lifetime of hardware used.

## Slide 91: Performance versus manufacturing footprint
Between 2017 and 2019 the Pareto frontier has shifted to the right prioritizing performance.
Designing sustainable systems requires shifting the frontier down.
Data from industry (Apple, Google, Huawei) life cycle analyses and GeekBench performance measurements https://www.geekbench.com/blog/2019/09/geekbench-5/
Performance and efficiency improvement
Notes: In fact, in the paper we show that it takes over 3 years of continuously running AI inferences on a Pixel 3 phone for the carbon footprint from energy consumption to equal that of hardware manufacturing.
3 years is the average life time of our mobile phones!
This highlights the need to extend hardware lifetimes through increased reliability and future proofing hardware to provide sufficient performance on emerging applications.
More generally, lower footprint devices are crucial towards a sustainable computing future.

## Slide 92: This work: ACT
Develop the model
Case studies

## Slide 93: This work: ACT
Develop the model
Case studies
More details in the paper!
Modeling parameters and industry sources for data
Carbon-aware metrics for early DSE (e.g., EDP, CDP, CEP)
Detailed comparison against industry LCA’s
Reuse case study: impact of reconfigurable accelerators (FPGA’s)
Recycle case study: Enabling second life & SSD provisioning

## Slide 94: This work: ACT
Develop the model
Case studies
Open-source!
More details in the paper!
Modeling parameters and industry sources for data
Carbon-aware metrics for early DSE (e.g., EDP, CDP, CEP)
Detailed comparison against industry LCA’s
Reuse case study: impact of reconfigurable accelerators (FPGA’s)
Recycle case study: Enabling second life & SSD provisioning

## Slide 95: Thank you!
Develop the model
Case studies
Open-source!
More details in the paper!
Modeling parameters and industry sources for data
Carbon-aware metrics for early DSE (e.g., EDP, CDP, CEP)
Detailed comparison against industry LCA’s
Reuse case study: impact of reconfigurable accelerators (FPGA’s)
Recycle case study: Enabling second life & SSD provisioning
This work: ACT

## Slide 96
Embodied carbon of application processors (SoC’s)
Fab energy increases over tech. nodes
DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)

## Slide 97
Embodied carbon of application processors (SoC’s)
Fab energy increases over tech. nodes
95% abatement
99% abatement
TSMC (97%)
DTCO including Sustainability: Power-Performance-Area-Cost-Environmental score (PPACE) Analysis for Logic Technologies. Bardon et. al (IEDM 2020)

## Slide 98
DRAM carbon per storage model
Data sources: SK Hynix
Notes: Just this section is around 8:30min

## Slide 99
SSD carbon per storage model
Data sources: SK Hynix, Apple
Notes: Just this section is around 8:30min

## Slide 100
More comparisons (ACT vs. LCA’s) in the paper…
 | ACT vs. Dell R740 server LCA | ACT vs. Fairphone 3 mobile device LCA

## Slide 101
More comparisons (ACT vs. LCA’s) in the paper…
Takeaways
ACT provides first-order approximate of LCA’s that use old technology nodes (45nm NAND, 32nm CPU)
ACT enables architects to study new technology nodes
IC component | ACT vs. Dell R740 server LCA | ACT vs. Fairphone 3 mobile device LCA
Compute (processors, SoC’s) | Within 2.2x | Within 1.18x
Memory | Within 1.62x | Within 2.1x
Storage | Within 1.05-2.2x | 

## Slide 102
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon

## Slide 103: Reduce: Designing leaner hardware systems
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
Architectural
Carbon Model
Performance/energy vs.
Carbon
2mm2 area
3x carbon decrease!
Nvidia DL Accelerator (NVDLA)

## Slide 104: Reduce: Designing leaner hardware systems
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
Architectural
Carbon Model
Performance/energy vs.
Carbon
2mm2 area
3x carbon decrease!
Nvidia DL Accelerator (NVDLA)

## Slide 105: Reduce: Designing leaner hardware systems
CO2 opt.
Energy
opt.
Performance
opt.
30 FPS target
Architectural
Carbon Model
Performance/energy vs.
Carbon
2mm2 area
30% carbon increase
(Jevon’s paradox)
3x carbon decrease!
Nvidia DL Accelerator (NVDLA)

## Slide 106
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon
Embodied CO2
Operational CO2

## Slide 107
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon
Embodied
reduction
Operational
degradation
Embodied CO2
Operational CO2

## Slide 108
Recycle: Extending hardware lifetime
Architectural
Carbon Model
Mobile SoC’s
Geekbench characterization
Operational vs.
Embodied carbon
Embodied
reduction
Operational
degradation
Embodied CO2
Operational CO2
Enabling 2nd life
requires enhancing
HW reliability
See paper for case
study on storage
reliability using
SSD overprovisioning